## Slide 1: 2G E/// Equipment Quantum Code Structure Issue 5.0
G6E3600idN71
  G – always a G for GSM
  6 – equipment platform – 6 (E/// 6000 series platform)
  E – vendor indicator - E (E///)
  3 – 900 layer, sector capability – 1, 2, or 3
  6 – 900 layer, number of Radio Units (RUS02)
  0 – 1800 layer, sector capability – N/A
  0 – 1800 layer, number of Radio Units – N/A
  id – equipment style, id/iL (Indoor DC RBS 6201); oa/oL (Outdoor AC RBS 6102); sc (Indoor DC ‘Standard Cube’ RBS 6202);
  ir (Indoor Remote DC RBS 6601; ob (Outdoor AC Cab 6140/50); od (Outdoor DC Cab 6320);
  ie (Indoor Eltek); oe (Outdoor Eltek); oy (Outdoor AC 6102 + York); ys (Outdoor All units in York/Shire cab);
  ib (Indoor DC Baseband);
  N71 – 1st character denotes ‘RF’ sharing of RUS; N = No RF Sharing; R = 1800 Band RF Sharing; S = 900 Band RF Sharing;
  T = 900 & 1800 Band RF Sharing;
  2nd character denotes Quantity of DUG; 1 = 3 x DUG20 (900 Only); 2 = 3 x DUG20 (900) + 1 x DUG20 (1800); 3 = 3 x DUG20 (900) + 3 x DUG20 (1800); 4 = 2 x DUG20 (900) + 2 x DUG20 (1800);
  5 = 1 x DUG20 (900) + 1 x DUG20 (1800); 6 = 2 x DUG20 (900) + 1 x DUG20 (1800);
  7 = 2 x DUG20 (900 Only); 8 = 1 x DUG20 (900 Only);
  9 = 1 x DUG20 (900 Only in Cab 6320); A = 1 x Mixed Mode BB6630 (2G + 3G);
  B = 1 x BB6630;
  3rd character denotes Type of RUS unit; 1 = RUS02 (900); 2 = RUS02 (900) and RUS01 (1800);
  3 = RUS02 (900) and RUS02 (1800); 4 = RRUS 12 (900);
  5 = Radio 2212 (900); 6 = Radio 2238 (900);
  .