## Slide 1: 3G E/// Equipment Quantum Code Structure Issue 5.4
U6E3618id0D3
  U – always a U for UMTS
  6 – equipment platform – 6 (6000 Series Platform)
  E – vendor indicator - E (E///)
  3 – number of sectors – 1, 2, or 3
  6 – number of carriers, either 2 (900 Only), 4 (2100 Only), or 6 (900 + 2100)
  18 – number of Power Amps (PAs)
  id – equipment Style, id (Indoor DC RBS 6201), oa (Outdoor AC RBS 6102), oc (Outdoor Retrofit Combination – U2100 in DC RBS6202; U900 Integral to RBS6102), sc (Indoor DC ‘Standard Cube’ RBS 6202), sm (Outdoor AC Small Cell RBS 6501), ir (Indoor DC RBS6601)
  0H7 – 1st character Spare 2nd character denotes Quantity & Type of DUW A = 1 x DUW31 (U9 OR U21) X = No Add’l BB Units B = 2 x DUW31 (U9 OR U21) G = 1 x BB5216 C = 1 x DUW31(U9) + 1 x DUW31(U21) H = 2 x BB5216 D = 1 x DUW31(U9) + 2 x DUW31(U21) E = 2 x DUW31(U9) + 2 x DUW31(U21)
        F = 1 x DUW31 (U9) + 2 x DUW 30 (U21)
  3rd character denotes Type of RUS Unit 1 = (RUS02 Only) A = U2100 (Radio2203) 2 = (RUS01 Only) B = U900 (R 2217 [RRU]) & U2100 (R 2217 [RRU]) 3 = U900 (RUS02) & U2100 (RUS01) C = U2100 (Radio 2217 [RRU]) 4 = U900 (RUS02 [6]) & U2100 (RUS01 [6])
  5 = U900 (RUS01) & U2100 (RRUS12 [RRH U2100])
  6 = U900 (RUS02) & U2100 (RRUS12 [RRH U2100])
  7 = U900 (RUS02) & U2100 (Radio 2217 [RRH])
  8 = U900 (RUS01) & U2100 (Radio 2217 [RRH])
  9 = U900 (Radio 2217 [RRH])